## Slide 2: DMC 21 team results
Each team had access to the infrastructure for 1 week
  Could tweak and tune, then run final tests
  At the end of the week, the team had a discussion with judges
Tests were set between specific DMC21 DTN sites
  IPv4 and IPv6, but two teams’ software did not support IPv6
Best results?
  Ciena-iCair-UETN team: UvA to NSCC 85Gbps, UvA to AARNet 84Gbps, memory to memory, and 25Gbps disk to disk
  Note: UvA’s DTN is hosted behind an Edgecore Wedge running RARE/FreeRtr – https://wiki.geant.org/display/RARE/Home

## Slide 3: Data Transfer Node (DTN) specs
DMC 21 had 9 organisations who kindly provided DTNs
  More are always welcome for the next DMC event
OS: CentOS 7 or Unbuntu 18-20
Memory: 4TB NVMe/SSD; XFS, RAID0; 2TB data set
100G network interface
Ansible used to automate configuration
  Software tools include Docker, perfSONAR, iperf3, Ethr, nuttcp
System tuned by Esnet’s ‘fasterdata’ guidance
  https://fasterdata.es.net/host-tuning/linux/100g-tuning/

## Slide 4: Specific DTN examples for the performant nodes
University of Amsterdam (UvA)
  Supermicro 6029U-E1CR4T, Ubuntu 18.04
  2 x Intel Xeon Gold 5122, 192 GB RAM. 8 x 1TB NVMe
National Singapore Computing Centre (NSCC)
  Supermicro SYS-2029U-TR4T 2 x Intel(R) Xeon(R) Gold 5122 CPU @ 3.60GHz
  2 x Mellanox Technologies MT27800 Family [ConnectX-5]
  4 x INTEL SSDPE2MD016T4 (1.6TB) NVMe SSD
  6 x 16GB (DDR4-2666)
  Ubuntu 18.04.54
AARNet
  Dell PowerEdge R7415 1 x AMD EPYC 7551P 32-Core Processor
  8 x 16GB DDR-4 2400 MHz 1 x BOSS-S1 223.51 GB (OS mirror)
  12 x Dell Express Flash NVMe P4600 1.6TB SFF (data Raid 0)
  OS Ubuntu 18.04.5
  Mellanox ConnectX-5 Single Port 100 Gb QSFP